## Slide 1: ME8492 KINEMATICS OF MACHINERY
FRICTION IN MACHINE ELEMENTS
Kalaiselvan.K
AP/MECH
Velammal Institute Of technology

## Slide 2: Bearings are machine elements
Bearings are designed to



reduce friction carry loads
guide moving parts

## Slide 3: What is Friction ?
Friction is resistance to movement
 it opposes sliding
 it assists rotation

## Slide 4: What is friction?
Plain bearings sliding friction
Rolling bearings rolling friction



## Slide 5: How did a bearing evolve ? Bearing history - a never-ending story
1100 B.C.
3500 B.C.
1995
1794
40 A.D.
1869

## Slide 6: How did a bearing evolve ?

## Slide 7: How did a bearing evolve ?
* Invention of wheel
Wheel rotates on axle
Wear Plate + Rollers
Inner ring + Outer ring
+ Rollers
With introduction of cage Rolling Bearing was created

## Slide 8: The components of a bearing
Seal
Rolling elements
Inner ring
Outer ring
Seal
Cage

## Slide 9: Bearing Basics
Pg. 7
Bearing Installation and Maintenance Guide

## Slide 10: Bearing Basics
BALL
POINT CONTACT
SPHERICAL
LINE CONTACT
TAPERED
LINE CONTACT

## Slide 11: Characteristics
Deep groove Angular ball bearing contact
ball bearing
Self-aligning ball bearing
Ball bearings
Point Contact :
*
*
*
*
Less area of contact Less friction
More speed Less load
Cylindrical roller bearing
Taper Needle
roller roller bearing bearing
Spherical roller bearing
Roller bearings
Line Contact :
*
*
*
*
More area of contact More friction
Less speed More load

## Slide 12: Rolling elements name the bearing
Spherical roller (symmetrical)
Ball
Spherical roller (asymmetrical)
Needle roller
Cylindrical roller
Taper roller

## Slide 13: Bearing loads
Radial load
Fr
Axial load
Fa
Combined load

## Slide 14: Radial rolling bearings
Radial rolling bearings
Deep groove ball bearing
Angular contact
ball bearing
Self-aligning ball bearing
Cylindrical roller bearing
Taper roller
Needle roller
bearing bearing
Spherical roller bearing
Ball bearings Roller bearings

## Slide 15: Thrust bearings
Thrust
ball bearing
Ball bearings Roller bearings
Angular Contact Ball Thrust bearing
Taper Roller Thrust bearing
Spherical Roller Thrust bearing
Cylindrical
/ Needle
Roller Thrust bearing

## Slide 16: Deep Groove Ball Bearing

## Slide 17: Bearings with shields and seals
Shields
Low-friction seals
Seals
-Z and -2Z
-RZ and -2RZ
-RS1 and -2RS1
Contaminant exclusion
Silent running
Grease retention
Speed capability

## Slide 20: Misalignment Parallel or offset misalignment Angular misalignment
Misalignments
produce additional stresses shorten bearing life increase seal wear increase vibration
increase noise
increase energy consumption
which will be avoided by proper shaft alignment or the use of a self-aligning bearing

## Slide 21
The industrial revolution has depended on a seldom recognized
component, the rolling bearing. So important is the rolling bearing that without it today's modern industry would
literally grind to a halt. From the beginning, SKF has led the world in
reducing friction with innovative rolling bearing solutions that have moved industry forward.
SKF was founded in Sweden in 1907 and grew out of Sven
Wingquist's solution to a misaligned drive shaft problem he faced in a textile mill. His invention of a double row self- aligning ball bearing was only the first of many innovations SKF has provided industry. From the first spherical rolling bearing to the current bearing life calculation methods used worldwide, SKF has pioneered the way with over 2,200 patents.

## Slide 23: Self Aligning Ball Bearing

## Slide 28: Bearing Basics

## Slide 30: Paired mounting increases load carrying capacity and stiffness of the bearing arrangement
Face-to-face arrangement
e.g. 71906/DF
Back-to-back arrangement
e.g. 71906/DB
Tandem arrangement
e.g. 71906/DT
Force acting on bearing or set Bearing stiffness (N/mm) = Elastic deformation due to load

## Slide 37: Double Row Angular Contact Ball Bearing

## Slide 38: Ball bearing properties
Deep groove ball bearing
Angular contact Self-aligning ball bearing ball bearing
radial load carrying capacity
axial load carrying capacity
speed capability
can accommodate misalignment

## Slide 39: Bearing Basics

## Slide 40: Cylindrical roller bearings
More and larger rollers
Logarithmic contact profile plus optimised surface finish
Improved roller end/flange contact geometry
3 cage variants: steel, polyamide, brass
NU
NUP
NJ
N
NJ+HJ
NU+HJ

## Slide 44: Bearing Basics

## Slide 45: Bearing Basics

## Slide 46: Bearing Basics

## Slide 47: Spherical roller bearings
Symmetrical rollers
for maximum life under any conditions
Floating guide ring gives minimum friction and ensures reliable operation
Window-type steel cages strong and tolerant to high temperatures

## Slide 51: Taper roller bearings
Taper rollers
for perfect rolling contact
Logarithmic profiled rollers
for protection from edge loading
Specially designed flange gives minimum friction and ensures reliable operation
Window-type steel cages strong and tolerant to high temperatures

## Slide 52: Single row and paired single row taper roller bearings
Single row
Face-to-face arrangement suffix DF
Back-to-back arrangement suffix DB

## Slide 53: Compact Aligning Roller Bearings CARBTM
Safer, more optimized design Increased service life
Lower running temperature Lower vibration and noise level Extended maintenance interval
Higher axial clearence No internal Friction force
Longer life Higher speed
Downsizing possibility

## Slide 54: CARBTM - Bearing Compact Aligning Roller Bearing
 Self-aligning as spherical roller bearing
 Permits axial displacements like a cylindrical roller bearing
 Compact as a needle roller bearing

## Slide 55: Thrust bearings
Thrust ball bearing single direction
Thrust ball bearing single direction with sphered housing washer
Thrust ball bearing double direction
Thrust ball bearing double direction with sphered housing washers
Cylindrical roller thrust bearing single direction
Spherical roller thrust bearing

## Slide 56: Spherical roller thrust bearings
Combined load carrying capacity Can take 55% of thrust load as radial load
Logarithmic profiled rollers
for protection from edge loading
Specially designed flange gives minimum friction and ensures reliable operation
Window-type steel cages strong and tolerant to high temperatures

## Slide 57: Compact Aligning Roller Bearings CARBTM
Safer, more optimized design Increased service life
Lower running temperature Lower vibration and noise level Extended maintenance interval
Higher axial clearence No internal Friction force
Longer life Higher speed
Downsizing possibility

## Slide 58: Bearings are precision products
Example: Tolerances for bore diameter 75 mm
Precision High precision
bearing bearing
Normal
Tolerance classes
Standa
rd
P6
P5 SP
P4A UP
PA9A PA9B
0/-7 m 0/-2,5 m
0/-15 m 0/-12 m 0/-9 m
How much is a m
1 
0,06 mm
A
human hair

## Slide 59: Materials for rolling bearings
Bearing rings and rolling elements
Through-hardening steels
Carbon chromium steel containing approximately 1 % carbon and 1,5 % chromium
Case-hardening steels
Chromium-nickel alloyed steel
Manganese-chromium alloyed steel
appr. 0,20 % carbon
SKF bearing steels have very high cleanliness
– the content of macro and microinclusions is extremely low.

## Slide 60: Cages keep the rolling elements separated
Prevent immediate contact between rolling elements to minimise friction and heat generation
Guide the rolling elements
Provide space for lubricant Serve to retain the rolling
elements when bearings of separable design are mounted or dismounted

## Slide 63: Cage variants
Polyamide cage
+ lightweight
+ high elasticity
+ good sliding properties
+ good marginal lubrication
properties
- operating temperature
limit +120°C
Window-type steel cage
+ lightweight
+ high strength
+ no operating temperature
limit
+ high vibration and
acceleration resistance
- sensitive to poor
lubrication
Window-type brass cage
+ very high strength
+ very high vibration and
acceleration resistance
+ suitable for very high
speeds in connection with
circulating oil lubrication
- relatively expensive

## Slide 65: Bearing clearance
Radial clearance
Axial
clearance

## Slide 67: Clearance
Normal clearance
Increased clearance because of temperature
Reduced clearance because of tight fit
Example:
6210/C3 = Deep groove ball bearing with clearance greater than Normal
CN does not normally appear in the bearing designation
Suffix clearance
/C1 less than C2
/C2 less than Normal
/CN Normal
/C3 greater than Normal
/C4 greater than C3
/C5 greater than C4